## Slide 1: 電気回路演習I Series and Parallel Circuit
水戸 慎一郎

## Slide 2: Electric Circuit: Today’s Focus
Why Circuits Work | Key Elements | What We’ll Compare
A Closed path lets electric charge flow. | Source: battery Conductors: wires Load: lamp | Series connections Parallel connections

## Slide 3: Series Resistors
loop 1
Pump
water level: High
Water Circulation
water level: Low
The same current passes through every resistor, but the total voltage is divided across them.
Resistors are in series when they are connected one after another in a single path. The output end of one resistor touches the input end of the next.
The same current flows through every resistor because there is only one route for the charges.
The battery’s voltage is shared (divided) across the resistors. Each one gets a part of the total voltage.
Applying Ohm’s law to each resistor: ,
Then, Applying Kirchhoff’s voltage law for loop:
So, we can define the total resistance by
Two resistors in series

## Slide 4: Parallel Resistors
Resistors are in parallel when their ends are tied to the same two nodes. Each resistor has its own branch, so there is more than one path for the charges.
Every branch sees the same voltage because both ends of each resistor touch the same pair of points.
The current splits up across the branches. The sum of the branch currents equals the total current from the source.
Applying Ohm’s law to each branch: and , they share the same voltage:
Next, use Kirchhoff’s current law at node a :
So, we can define the total resistance by
Two resistors in parallel
a
The current splits between the resistors, but each resistor has the same voltage across it.
Pump
Water Circulation

## Slide 5: Equivalent Resistance (Total Resistance)
Equivalent resistance in series
Equivalent resistance in parallel
When resistors are connected in series, their equivalent resistance is simply the sum of their individual resistances.
When resistors are connected in parallel, the reciprocal of their equivalent resistance equals the sum of the reciprocals of their individual resistances.
For the special case of two parallel resistors, that rule can be rearranged into the “product over sum” shortcut.

## Slide 6: Exercise
(1)
(2)
(3)
(4)
(5)
(6)
Q1. Find the total resistance.

## Slide 7: How to Find in Complex Resistors Network
Example of complex resistors network
To find the total resistance of a complex circuit, we combine resistors step by step using series and parallel rules.
1) First, calculate as the parallel combination of 6 Ω and 3 Ω:
2) Next, add 2 Ω in series with ​ ​to get ​. Also, combine the 1 Ω and 5 Ω resistors in series to get ​.
Now, ​ and ​ are connected in parallel, so the total resistance can be calculated using ​and ​:
3) Finally, 4 Ω, ​, and 8 Ω are in series:

## Slide 8: Exercise
(1)
(2)
(3)
(4)
“short-cut”
“opened”
Q2. Find the total resistance.

## Slide 9: Exercise
a
b
24kW |  | 
16kW |  | 
30kW |  | 
90kW |  | 
24kW |  | 
16kW |  | 
30kW |  | 
90kW |  | 
Q3. Find the total resistance and complete a table following when 642 V of voltage is applied across a-b.

## Slide 10: Voltage Divider Rule (Series Circuit)
Series circuit (Voltage divider)
Same current flows through both resistors because they are in series.
By Ohm’s law:
Kirchhoff’s voltage law gives:
Eliminate to get the voltage divider rule:
Find voltage without current!

## Slide 11: Current Divider Rule
Two resistors in parallel
(Current divider)
a
Same voltage on each branch:
Ohm’s law for each resistor:
Express the supply voltage in terms of the total current
Substitute back into the branch currents
Find branch current without solving for !

## Slide 12: Exercise
a
Q4. For the circuit shown in picture, find...
  Total resistance R
  Voltage and by voltage division
  Current and by current division

## Slide 13: おまけ Optional Exercise
3つの抵抗、 、 のすべての接続方法に対して、合成抵抗を求めよ。
Determine the equivalent resistance for every possible way of connecting three resistors , , and .
6 Ω
0.545 Ω
2.2 Ω
2.75 Ω
3.67 Ω
0.833 Ω
1.33 Ω
1.5 Ω